## Slide 1: ASAIC OVERVIEW
April 30, 2014
Saab Sensis Corporation

## Slide 2: Introduction
Saab Sensis has surface and terminal data expertise
  Prime contractor for ASDE-X, ASSC & RWSL systems
  Numerous techniques to extract information
  Ability to improve accuracy
  Automated event detection tools and capabilities
Safety
  “Hot spot” identification to focus effort
  Anomalous behavior recognition and trending
  Unreported events made visible
Efficiency
  Fuel burn
  Environmental impact
  Economic savings
Analytical work
  Analysis
  Case studies
  Benefits studies

## Slide 3: Saab Sensis ASDE-X/ASSC/RWSL Sites
Saab Sensis is the expert in airport surface surveillance
SEA
PHX
SLC
LAS
LAX
SNA
IAH
DFW
DEN
HNL
MSP
STL
MEM
ATL
MCO (RWSL Key Site)
FLL
MIA
CLT
MKE (ASDE-X Key Site)
ORD
MDW
DTW
BOS
PVD
BDL
JFK
LGA
EWR
PHL
BWI
DCA
IAD
SAN
HOU
SDF
PDX
SFO (ASSC Key Site)
ANC
MSY
MCI
CVG
CLE
PIT
Key
ASDE-X (13)
ASDE-X & RWSL (22)
ASSC (8)
ASSC & RWSL (1)

## Slide 4: Track Joining and Smoothing
BLUE: Track Reconstruction (Ver. 3)
GREEN: Track Reconstruction (Ver. 4)
BLACK: MLAT Position Data
RED: SMR Position Data
Post processing yields more accurate position estimates

## Slide 5: Metrics and Measurements
  Saab Sensis has developed algorithms to convert ASDE-X data into information.
  We create continuous tracks from the airport surface out to approximately 60 nautical miles from system center.
  Saab Sensis have processed over 15,000 days at the 35 ASDE-X airports.
  Examples of the type of information Saab Sensis can extract from the ASDE-X includes:
Taxi times
Duration and location of surface delays
Ramp and runway usage
Arrival/departure rates
Ground vehicles tracks
Vehicle velocity and acceleration
Vehicle heading and orientation
Routes used
Wheels up/wheels down
Anomalous events
Many other metrics….
Saab Sensis has created a reliable system to process surveillance data

## Slide 6: Automated Anomaly Detection and Scoring
Sudden stop
Irregular turn
“Missed” departures
“Missed” arrivals
Wake vortex
Runway incursion
Conflict risk
Route excursion
Runway transition
Long taxi times

## Slide 7: The Viewer
Saab Sensis has constructed a processing/playback/analysis tool.

## Slide 8: Study: ATL Arrival Surface Delays During 2010
  Total arrivals: 351,210 arrivals
  A hold is any stoppage by an aircraft in the movement area which lasts more than 10 seconds:
  Total number of holds: 313,955 holds
  Average number holds per arrival: 0.67
  Typical hold time (mode): 1.75 minutes
  Total time spent in holds during 2010: 381 days
  Cost due to holds ($35/min): $19.2 million dollars
  A “long” hold is any hold greater than 10 minutes. A long hold is typical due to the unavailability of a gate or the ramp entrance being blocked:
  Total number of long holds: 5,477 holds
  Total time spent in long holds: 60 days
  Cost due to long holds ($35/min): $3 million dollars
Analyses can identify potential efficiency improvements

## Slide 9: Example: Automated Determination of Anomalous Events (Sudden Stops)
Sudden Stop
Automated detection of anomalous events
Notes: Irregular Turn Set 1 Example 1

## Slide 10: Study: Sudden Stop Impact
Non-anomalous departures
Departures with sudden stop anomalies
Congestion
Taxi Time (minutes)
Study period: 2010
Study airport: JFK
Analysis identifies potential safety and efficiency improvements
Elevated sudden stop clustering
1 StD above mean
Major clustering
2 StD above mean
Each dot represents the location of a hard braking event during 2009.

## Slide 11: Example: Finding Associated Anomalies
Irregular Turn
Sudden Stop
Automated detection of coupled anomalous events
Notes: Irregular Turn Set 1 Example 1

## Slide 12: Example: “Missed” Departure
Departing aircraft
Taxiing aircraft
High acceleration rejection
Automated detection of anomalous events and causality

## Slide 13: Study: “Missed Arrival” ATL Taxiway Landing
Lined up on 27L
Given clearance to switch to 27R
Lands on taxiway
3D view
Detected as “missed” arrival since the aircraft lined up for arrival but never used a runway
Automated detection of unstable approaches

## Slide 14: ATL End-Around Study (CRJ2 departures only)
Departure reaches Victor
Arrival taxiing on Victor
262 meter separation
From surveillance compute the minimum distance between every arrival-departure pair.
Distance (meters) | Probability
10 | 1.30E-10
20 | 6.20E-10
30 | 2.78E-09
40 | 1.14E-08
50 | 4.32E-08
Use an Extreme Value Distribution to predict distance probabilities.

## Slide 15: CONFIRMING RUNWAY EXIT STUDY
CONCLUSIONS:
ASDE-X could be used to confirm clearance of runway edge with confidence determined by the buffer distance.
Displayed icon size is biggest source of error.
Some of performance outliers are due to missing wake category information (use of “normal” icon for heavy).
ASDE-X data can also be used to quantify the predictability of aircraft movement from the runway edge to clearing any specified safety zone boundary.

## Slide 16: Operations Counts by Airport (October 2012)
Mean daily operations counts for the 35 ASDE-X airports for October 2012. The mean is represented by the red line. The blue box represents 1 standard deviation and the dashed line is 3 standard deviations..
Red dots are outliers for the month. October 29-30 is the date for hurricane Sandy
Secondary effects from hurricane Sandy at Orlando and Miami.

## Slide 17
35 Airports, 14+ Months Processed
ASAIC- Airport Safety Anomaly Investigation Capability

## Slide 18: Operational Statistics (Hourly and outlier metrics)
Playback the busiest
hour of the year
Identify abnormal
days

## Slide 19: Monthly Anomaly Cluster Map
Shows locations on the airport surface where rates of anomaly candidates occur most often.

## Slide 20
Monthly Metrics
Clickable Drilldown

## Slide 21
Daily Metrics

## Slide 22
Taxi Times
Excessive taxi times due to heavy thunderstorms.

## Slide 23: Missed Arrivals
Anomaly playback
Add user comments

## Slide 24: Video Playback of Anomalies

## Slide 25: Missed Departure Stats
Numerous “Long Taxi Time” anomalies during the thunderstorm
Peak runway rate shows massive queue as storm moves in.
Clickable comment show playback

## Slide 26: Surface Anomaly Candidates
Surface anomaly candidates including: sudden stops, irregular turns, runway transitions and 9 other types.
Hover over list to show the location, click to playback
High scoring anomaly candidates are shown.